CELARE BY DIGILOCK PHENOLIC LOCKER SPECIFICATION

Section 10 51 00

- Applies to one wide, 1 tier (1W1T) Celáre Lockers with laminated phenolic doors in France Sycamore color with a glossy texture and Digilock 4G ATS keypad locks.

PART 1 – GENERAL

1.1  SUMMARY

Furnish and install Celáre laminated phenolic lockers with installed electronic locks as shown or indicated on approved drawings.

1.2  SUBMITTALS

Provide in accordance with submittal procedures:

Lockers:  Submit drawings showing locker types, sizes and quantities, including all necessary details relating to anchoring, trim installation and relationship to adjacent surfaces.

Locks:  Submit product data for locks including lock type, orientation, lock interface, quantities and all necessary details related to installation instructions.

Lock Management:  Indicate lock management by key and required number of keys to be delivered directly to owner’s representative.

PART 2 – PRODUCTS

  - MANUFACTURER:

Digilock 9 Willowbrook Court, Petaluma, CA 94954; 800-989-0201; www.digilock.com.  Requests to use equivalent products of other manufacturers shall be submitted in accordance with Product Substitution Procedures and may be approved provided they meet the detailed written specifications below.

2.2 LOCKERS:

The locker frame shall not be larger than 16”w x 20”d x 76”h.

-OPTION 1: The locker shall be one wide, with two openings per tier (1W-2T).

-OPTION 2: The locker shall be one wide, with three openings per tier (1W-3T).

-OPTION 3: The locker shall be one wide, with six openings per tier (1W-6T).

-OPTION 4: The locker shall be two wide, with one opening per tier (2W-1T).

-OPTION 5: The locker shall be two wide, with two openings per tier (2W-2T).

-OPTION 6: The locker shall be two wide, with three openings per tier (2W-3T).

-OPTION 7: The locker shall be two wide, with six openings per tier (2W-6T).

2.2.1 Materials: All major steel parts shall be made of milled cold rolled steel capable of taking a pantone solid coated paint (body parts). All major phonolic parts shall be high pressure laminate material.

2.2.2 Finish: Surfaces of steel shall be cleaned and prepared for finish in accordance with manufacturer’s instructions.

2.2.3 Door Frames: Door frames shall be integrated with locker uprights in channel shape, providing a continuous vertical door strike.

2.2.4 Phenolic Doors: Doors shall be .46” (11.8 mm) thick high pressured laminate. Door shall contain formation and punching to accept recess mount Digilock 4th generation ATS and APS product lines.

2.2.6 Hinges: Hinges shall be Euro-style soft close hinges, with high-bond adhesive attachment to door and mechanical attachment to frame and guaranteed to operate a minimum of 80,000 openings.

2.2.7 Body Components: All locker body components shall be 20 gauge steel. Tops, bottoms and shelves are flanged on all four sides and riveted to uprights/frame and back. Backs shall contain two sections of square perforations to provide full ventilation of locker interior. Single, double and triple tier lockers include two single prong hooks. Single tier lockers include coat rod.

2.2.8 Number Plates: Self-adhesive number plates in number series as provided by owner or owner’s representative are supplied for application to door in field.

2.2.9 Color: All locker body components shall be finished in color 02 Charcoal Grey. Laminated phenolic locker doors are supplied in France Sycamore color (8746-65). Specifier may choose from the following standard finishes:

-OPTION 1: Specifier may specify Waterfall (10501-65).

-OPTION 2: Specifier may specify Silver Wenge (8218-65).

-OPTION 3: Specifier may specify Cookie Teak (10235-65).

-OPTION 4: Specifier may specify Alabaster (906-65).

-OPTION 5: Specifier may specify Silver Blue (824-65).

-OPTION 6: Specifier may specify Bamboo Leaf (899-65).

-OPTION 7: Specifier may specify Inca Gold (943-65).

-OPTION 8: Specifier may specify Ruby (946-65).

-OPTION 9: Specifier may specify an alternate color from the Core Design Book.

2.2.10 Texture: Phenolic locker doors are supplied with a glossy texture (01). Specifier may choose from the following standard textures:

-OPTION 1: Specifier may specify Matte texture (02).

-OPTION 2: Specifier may specify Super Matte texture (52).

-OPTION 3: Specifier may specify Hi Texture texture (65).

-OPTION 4: Specifier may specify Straight-Fine Lines texture (41).

-OPTION 5: Specifier may specify Embossed texture (70).

-OPTION 6: Specifier may specify Natural Woodgrain texture (30).

-OPTION 7: Specifier may specify Plain Woodgrain texture (31).

-OPTION 8: Specifier may specify Quarter Woodgrain texture (32).

-OPTION 9: Specifier may specify alternate texture from the Core Design Book.

2.2.11 Assembly:  Lockers shall be fully assembled prior to delivery using rivets for a strong mechanical connection.

2.3 LOCKS

2.3.1 Type:  The lock shall be a Digilock 4th generation ATS recess mount keypad operated electronic lock.

-OPTION 1: Specifier may specify Diglock 4th generation ATS recess mount RFID operated electronic lock.

-OPTION 2: Specifier may specify Diglock 4th generation APS recess mount keypad operated electronic lock.

-OPTION 3: Specifier may specify Diglock 4th generation APS recess mount RFID operated electronic lock.

See ATS and APS lock specifications for details.

PART 3 – EXECUTION

3.1 DELIVERY AND INSTALLATION

Deliver lockers in manufacturer’s original, labeled cartons. Lockers must be installed in accordance with owner’s approved drawings and installation instructions. Installation shall be level such that lock operates without binding.

3.2 PROGRAMMING

Upon completion of installation, inspect locks for proper factory default operation. Transfer programming and electronic manager key(s) to owner.

3.3 QUALITY ASSURANCE

Digilock reserves the right to modify the design and/or function of lock and locker or change specifications to maintain compliance with corporate quality assurance policies.